AN EXECUTIVE SUMMARY OF THE MGB RAPID FIELD ASSESSMENT

OF LANDSLSIDE PRONE BARANGAYS OF SURIGAO DEL NORTE

In fulfillment of the Mines and Geosciences Bureau (MGB)’s commitment to finish the geohazard assessment of Surigao del Norte, five (5) geologists, two (2) from the Lands Geological Survey Division (LGSD) of the MGB Central Office in Quezon City, one (1) from MGB Region IV-A, one (1) from MGB Region IV-B and one (1) from MGB Region XIII, conducted a rapid field assessment of landslide prone barangays in all the municipalities in mainland of Surigao del Norte from June 24 to July 12, 2006.

The rapid field assessment focused on barangays that are located on footslopes, mid slopes and mountain ridges. Each barangay was rated with low, moderate or high landslide susceptibility. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks that would directly affect the community

- Areas with drainages that are prone to landslides damming

- Steep slopes

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks and are located away from the community

- Moderate slopes

Low

- Low to gently sloping

- Absence of tension cracks

There are a total of one hundred ninety-five (195) barangays assessed not only for landslide occurrence but also for flooding susceptibility in some areas. The result of the MGB Rapid Field Assessment is as follows:

- 45 barangays have a high landslide susceptibility;

- 52 barangays have a moderate landslide susceptibility;

- 50 barangays have a low landslide susceptibility; and

- 44 barangays have no/ none landslide susceptibility

The appropriate barangays were presented with a Landslide Threat Advisory. The Advisory informs the barangays of their susceptibility to landslides and have the corresponding recommendations particular to the barangay. The flood susceptible barangays were also given suitable recommendation.

Table 1.

Number of Assessed Barangays in Mainland Municiaplities in Surigao del Norte

| Municipality | Total Numberof Barangays | Barangays Assessed |
| --- | --- | --- |
| 1. Alegria | 12 | 12 |
| 2. Bacuag | 9 | 9 |
| 3. Claver | 14 | 14 |
| 4. Gigaquit | 13 | 13 |
| 5. Mainit | 21 | 21 |
| 6. Malimono | 14 | 14 |
| 7. Placer | 20 | 17 |
| 8. San Francisco | 11 | 11 |
| 9. Sison | 12 | 12 |
| 10. Surigao City | 54 | 54 |
| 11. Taganaan | 14 | 9 |
| 12. Tubod | 9 | 9 |
| TOTAL | 203 | 195 |

Table 2.

Number of Barangays Per Landslide Susceptibility Rating

| Municipality | Landslide Susceptibility Rating | Total |
| --- | --- | --- |
|  | High | Moderate | Low | None |  |
| 1. Alegria | 2 | 4 | 2 | 4 | 12 |
| 2. Bacuag | 3 | 2 | 3 | 1 | 9 |
| 3. Claver | 1 | 3 | 4 | 6 | 14 |
| 4. Gigaquit | 0 | 2 | 4 | 7 | 13 |
| 5. Mainit | 3 | 4 | 7 | 7 | 21 |
| 6. Malimono | 5 | 6 | 3 | 0 | 14 |
| 7. Placer | 5 | 3 | 4 | 5 | 17 |
| 8. San Francisco | 6 | 2 | 2 | 1 | 11 |
| 9. Sison | 2 | 2 | 8 | 0 | 12 |
| 10. Surigao City | 16 | 19 | 13 | 6 | 54 |
| 11. Taganaan | 2 | 2 | 2 | 3 | 9 |
| 12. Tubod | 0 | 3 | 2 | 4 | 9 |
| TOTAL | 45 | 52 | 50 | 44 | 195 |

SUMMARY OF THE ASSESSMENTS:

Table 3.

Summary of Assessment of the Municipality of ALEGRIA

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Camp Edward | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 2. Ferlda | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Constant communication and updates with Municipal Disaster Coordinating Council on geohazard situtation in the area (especially on Purok 1) |
| 3. Alipao | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Do not allow structures/residences to be built in landslide prone areas of Ben12 and Lillia |
| 4. Budlingin | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; |
| 5. Pongtud | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks) along National Highway particularly in Purok 5 |
| 6. San Juan | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 7. Ombong | Low |  |
| 8. San Pedro | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Activate BDCC in your area; Do not allow structures/ housing residences in landslide prone areas in Magja. |
| 9. Anahaw | None | Flooding hazard was noted at Purok 3 |
| 10. Don Julio Ouano | None |  |
| 11. Gamuton | None |  |
| 12. Poblacion | None |  |

Table 4.

Summary of the Assessment of the Municipality of BACUAG

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Cabuayon | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Brgy officials and residents should be vigilant in observing their area especially during abnormal, intense rainfall; Do not allow structures/houses to be built in landslide prone areas |
| 2. Payapag | High | Monitor progress of mass movement (e.g. landslides, tension cracks) on upslopes of Purok 1 and 2; Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Mobilize BDCC in your area; Alert people living near slope during heavy continuous rainfall; |
| 3. Poblacion | Low at Brgy. Proper in Poblacion; High at Purok Laurel | Monitor progress of mass movement (e.g. landslides, tension cracks) at Purok Laurel; Observe for presence of mass movement (e.g. landslides, tension cracks); Activate BDCC in your area; Warn residents of Purok Laurel on possible landslide threats |
| 4. Campo | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; Constant communication and updates with Brgy. Cabugao on geohazard situation; |
| 5. Pongtud | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks) in Kabalisan area; Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Constant communication and updates with Brgy.Cambuayon on geohazard situation; Activate BDCC in your area and mobilize its members during heavy continuous rainfall; Alert people living near slope and river bank; |
| 6. Dugsangon | low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 7. Pautao | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Activate BDCC in your area; |
| 8. Sto. Rosario | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 9. Cabugao | None |  |

Table 5.

Summary of the Assessment of the Municipality of CLAVER

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Wangke | High | Monitor progress of mass movement (e.g. landslides, tension cracks) in Purok 4; Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Brgy. officialsand residents should be vigilant in observing the possible landslide occurrence during intense abnormal rainfall. |
| 2. Sapa | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Organize BDCC to monitor progress of mass movement in Purok 3; |
| 3. Taganito | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks) especially at Sitio Pitugo and minesite; Observe for presence of mass movement (e.g. landslides, tension cracks) at Sitio Pitugo and minesite; Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 4. Urbiztondo | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks) on hills and roadcuts; Mobilize BDCC during continupous heavy rains and alert people/residents along the roadcuts and slopes for the possible slope failure |
| 5. Cabugo | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks) along National Highway particularly in Purok 5 |
| 6. Cagdianao | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Evacuate residents of coastal houses during tropical cyclone |
| 7. Daywan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 8. Lapinigan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Evacuate residents near the shore to safer elevated areas during tropical cyclone |
| 9. Bagacay | None | Flooding hazard was noted at Purok 3 |
| 10. Hayanggabon | None | Construct proper drainage system (large diameter culvert) along Purok 1, 2 and 3 in Brgy. Hayanggabon |
| 11. Magallanes | None |  |
| 12. Panatao | None |  |
| 13. Tayaga | None |  |
| 14. Ladgaron | None at barangay proper; Low at Purok 5 | FOR PUROK 5: Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); |

Table 6.

Summary of the Assessment of the Municipality of GIGAQUIT

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Caman-oman | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks) in Sitio Katikuyan; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; |
| 2. Mahanub | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 3. Camboayon | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 4. Lahi | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; |
| 5. San Isidro | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Activate BDCC in your area; |
| 6. Sico-Sico | Low | Observe for presence of mass movement (e.g. landslides, tension cracks) Sitio Sug-ong; Observe for saturated ground or seeps in areas that are not typically wet |
| 7. Alambique | None | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 8. Anibongan | None |  |
| 9. Ipil | None |  |
| 10. Poniente | None | Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 11. San Antonio | None |  |
| 12. Villaflor | None | Identify evacuation site; |
| 13. Villafranca | None |  |

Table 7.

Summary of the Assessment of the Municipality of MAINIT

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Paco | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Mobilize BDCC during heavy, continuous rains and alert residents living near footslopes; |
| 2. San Francisco | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Activate BDCC in your area; |
| 3. Tolingon | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Mobilize BDCC and alert residents near the footslopes during rainy season |
| 4. Binga | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for saturated ground or seeps in areas that are not typically wet; |
| 5. Bobona-on | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Alert people living near the edge of the river valley slope (Hinaksuynan River) during heavy and continuous rains.tension cracks); Develop an early warning device/system; |
| 6. Mansayao | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 7. Silop | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for saturated ground or seeps in areas that are not typically wet; |
| 8. Cantugas | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 9. Dayano | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 10. Marayag | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 11. Roxas | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Activate BDCC in your area; |
| 12. San Jose | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 13. Siana | Low | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 14. Tagbuyawan | Low | Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 15. Mabini | None |  |
| 16. Magpayang | None | Identify evacuation site for Purok 2 |
| 17. Magsaysay | None |  |
| 18. Matinao | None |  |
| 19. Quezon | None | Identify evacuation site; |
| 20. Tapian | None | Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 21. San Isidro | None |  |

Table 8.

Summary of the Assessment of the Municipality of MALIMONO

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Karihatag | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for saturated ground or seeps in areas that are not typically wet; Alert people living near the foot of the slope (Purok 4) during heavy rainfall |
| 2. Masgad | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Alert the people living near the base of the slope or footslopes during continuous, heavy rainfall |
| 3. Pili | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 4. Tinago | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; |
| 5. Villa Riza | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; |
| 6. Binocaran | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 7. Cagtina-e | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 8. Can-aga | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; |
| 9. Cansayong | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; |
| 10. Cantapoy | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 11. San Isidro | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 12. Bunyasan | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 13. Cayawan | Low |  |
| 14. Hanagdong | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); |

Table 9

Summary of the Assessment of the Municipality of PLACER

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Bad-as | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Activate BDCC during extreme weather condition; |
| 2. Bugas-Bugas | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; |
| 3. Central | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate amnd organize the BDCC in your area; Relocate residents in Puroks Mahigogmaon, Gaway-gaway, Sitio Jagimitand other landslide prone areas; Barangay officials and residents should be vigilant in observing landslides especially rainy season; An extensiometer should be placed in tension cracks to monitor its progression; |
| 4. Ipil | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 5. Magsaysay | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for saturated ground or seeps in areas that are not typically wet; If possible relocate residents in Purok Diamond Hills; Be vigilant in observing landslide prone areas especially during rainy season/intense abnormal rainfall; An extensiometer should be placed in tension cracks to monitor the movements in cracks |
| 6. Amoslog | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 7. Anislagan | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 8. Panhutongan | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; |
| 9. Boyongan | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); If possible avoid structures/houses on areas (in Purok 1) where tension cracks were observed/reported; |
| 10. Magupangi | Low |  |
| 11. San Isidro | Low |  |
| 12. Suyoc | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 13. Mabini | None | Avoid building houses at the foot of identifiedunstable ground (outskirt of Purok 3) |
| 14. Macalaya | None |  |
| 15. Pananay-an | None |  |
| 16. Sta. Cruz | None | Identify evacuation site for Purok 2 |
| 17. Tagbongabong | None |  |

Table 10.

Summary of the Assessment of the Municipality of SAN FRANCISCO

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Magtangali | High | Monitor progress of mass movements (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in area that are not typically wet; Alert BDCC during continuous heavy rains and alert people living along the slopes (Sitio Brasil) |
| 2. Oslao | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify other evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Constant communication and updates with Brgy. Balite on geohazard situation; Set-up extensiometer to monitor movement (Puroks 1 and 4); Immediate and temporary evacuation during heavy rainfall; Activate BDCC in your area. |
| 3. Jubgan | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Activate BDCC in your area |
| 4. Amontay | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Activate BDCC in your area |
| 5. Linongganan | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Activate BDCC in your area |
| 6. Balite | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Activate BDCC in your area |
| 7. Macopa | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; alert people living near footslope during continuous heavy rainfall |
| 8. Banbanon | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; no residential structures should be built from Purok 3 to Banderahon; Brgy. Officials and residents should be vigilant especially during intense prolong rainfall |
| 9. Honrado | Low | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Be alert especially when intense continuous rainfall occurs |
| 10. Poblacion | Low | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity |
| 11. Diaz | None (Brgy. Proper); moderate (Purok VI) | Monitor progress of mass movement at Purok VI (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; Monitor weather condition; For Purok VI - Evacuation during heavy rainfall, Warn residents of possible debris flow (landslide) and flooding occurence during heavy rainfall, Coordinate with BDCC |

Table 11

Summary of the Assessment of the Municipality of SISON

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Gacepan | High | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for saturated ground or seeps in areas that are not typically wet; Mobilize BDCC during heavy and continuous rainfall; Alert people living at the base of the slope and near the river/creek mouths |
| 2. Mayag | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Mobilize BDCC during heavy continuous rainfall; Alert residents near the base of the slopes and creek/river mouths |
| 3. Mabuhay | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for sunken or displaced road surfaces; |
| 4. San Pedro (Poblacion) | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Warn residents of Puroks 6 and 8 on the threat of landslide; Alert people of barangay proper on the threats of flooding during rainy seasons; Consult MGB-XIII on the possible geohazards in the municipal relocation site at Purok 8 |
| 5. Biyabid | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 6. Ima | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 7. Lower Patag | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |
| 8. San Isidro | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 9. San Pablo | Low | Monitor progress of mass movement (e.g. landslides, tension cracks); |
| 10. Tagbayani | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 11. Tinogpahan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; |
| 12. Upper Patag | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); |

Table 12

Summary of the Assessment of the Municipality of SURIGAO CITY

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Bonifacio | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for sunken or displaced road surfaces; stabilize the slopes of National Maharlika Highway at Km. 6; re-routing of National MAharlika Highway to avoid the active landslide and river bank scouring at Km. 6; appropriate and proper engineering measures should be applied at National Maharlika Highway at Purok 1 where riverbank scouring is active |
| 2. Canlanipa | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; |
| 3. Lipata | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in the area |
| 4. Punta Bilar | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Activate BDCC in the area |
| 5. Quezon | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site for Puroks Nangka and Narra; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Activate BDCC in the area |
| 6. Rizal | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Alert people living at the toe of the slope/footslope especially at Sitio Balibangon during continuous rains; Other sitios with reported tension cracks are Sitios Lumaban, Tumandag and Kinabutan 2 should closely monitor the progress of tension cracks. |
| 7. Taft | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); In Purok Kalipayan, if possible relocate 15 houses to be affected by landslide; Imposition of easement regulation along shoreline; Provision of engineering measures to control extent of flooding; Rationalization of urban land development planning suited to the geohazards conditions of the city; Flooding- Implementation of Integrated Surigao City flood mitigation program. |
| 8. Togbongon | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Alert people living along footslopes during continuous heavy rainfall |
| 9. Washington | High | Monitor progress of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; If possible, relocation of residents located on Candava Hill, if not residentsresidents and barangay officials are advised to be vigilant especially during continuous intense rainfall; Implement engineering measures to prevent landslides and/or flooding; No structures to be built along the roadside nof the hill; Land-use for residential purposes should be regulated by the LGU; Imposition of easement regulation along riverbanks and estuaries; Moratorium in the reclamation and expansion for urban settlement in highly-flood prone areas; Rationalization of urban land development planning suited to the geohazard condition of the City. |
| 10. Capalayan | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area |
| 11. Danao | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Organize BDCC and mobilize the members during continuous heavy rainfall to monitor the possibility of landslide |
| 12. Ipil | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks);Develop an early warning device/system; Identify evacuation site; Activate BDCC in your area; Warn residents on possible occurrence of landslide in Sitio Palhi during heavy rainfall and coordinate with the BDCC |
| 13. Luna | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Activate BDCC in the area; Alert residents of Vicente , Sitio Looc, Peace, Faith, and Springville on the possible landslide ocurrence; Identify evacuation sites on the Puroks and Sitios identified prone to landslide |
| 14. Mapawa | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site and safe escape routes since the concentration of hazards are along the main routes of Mapawa; Activate BDCC in the area |
| 15. Poctoy | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks); alert residents living near footslopes especially in Puroks 4 and 5 during heavy rainfall. |
| 16. San Roque | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks);Observe for saturated ground or seeps in areas that are not typically wet; Always alert residents especially in Purok 1 and 2 during continuous heavy rains for possible landslides; mobilize BDCC during heavy rains. |
| 17. Sukailang | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for sunken or displaced road surfaces; stabilize the slopes |
| 18. Trinidad | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for sunken or displaced road surfaces; stabilize the slopes; An extensiometer maybe emplaced as a monitoring tool |
| 19 Cabongbongan | Low |  |
| 20. Cagniog | Low |  |
| 21. Mabini | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 22. Mabua | Low | Observe for presence of mass movement (e.g. landslides, tension cracks) |
| 23. Nabago | Low |  |
| 24. Orok | Low |  |
| 25. Serna | Low | Monitor progress of mass movement (e.g. landslides, tension cracks);Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 26. Mat-i | Low; Moderate on uplands | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for mass movement on purok areas on uplands; monitor progress of mass movement/tension cracks reportedly located at Purok Pinaypayan, Sitio Bumbaran |
| 27. Balibayon | Low |  |
| 28. Anomar | None | Activate BDCC in the area |
| 29. Day-asan | None |  |
| 30. Sabang | None | Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); possible formulation of Integrated Surigao River Flood Mitigation Program is highly imperative; Houses must be elevated that the residents may not experience or minimize flooding in Purok 1; If possible, relocate/evacuate areas in Puroks 2, 3 and 4 to evade possible occurrences of tidal storm/storm surge in times of extreme weather condition. |
| 31. San Isidro | None |  |
| 32. San Juan | None | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Detailed geo-environmental study of the dynamics and natural cycles and process of the Surigao River and other flood prone areas; Easement regulation along riverbanks; If possible, relocation of houses along the critical zone of flooding; provision of engineering measures to control extent of flooding; organizationand actiation of BDCC; Dredging of Surigao River |
| 33. Silop | None | Retaining walls/gabions/riprap structures can be constructed t prevent further encroachment of the creek's bank; another option is to relocate the single house that would be affected to a much stable area, if possible |
| 34. Alang-Alang | Moderate; High at Purok 3 | Monitor progress of mass movement (e.g. landslides, tension cracks)especially at Purok 3. Observe for presence of unstable slope due to wave-cut erosion. Activate Barangay Disaster Coordinating Council (BDCC) in other hazards that may occur (e.g. storm surge, tsunami) |
| 35. Alegria | Low | Activate Barangay Disaster Coordinating Council (BDCC) in other hazards that may occur (e.g. storm surge, tsunami) |
| 36. Aurora | Low; Moderate at Purok 3 | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Installation of signage at the periphery of a previous landslide and restrict future settlement in the area. Activate Barangay Disaster Coordinating Council (BDCC) in other hazards that may occur (e.g. storm surge, tsunami) |
| 37. Baybay | High esp. at Purok 3 (Sitio Panuyboyon) | Monitor and observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Evacuation of residents especially at areas near base of slope in Sitio Panuyboyon where at least 5 houses are at projected path of a potential debris slide. Activate BDCC during periods of inclement weather condition. |
| 38. Bilabid | Low; Moderate at Purok 2 | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of unstable slope due to wave-cut erosion. Activate Barangay Disaster Coordinating Council (BDCC) in other hazards may occur (e.g. storm surge, tsunami) |
| 39. Bitaugan | High esp. at Purok 1 and 2 | Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Evacuation of residents especially at areas near base of slope during periods of heavy rains. Long-term relocation to a safer site away from slopes (such as coastal reclamation of the southeast portion of the barangay). Installation of landslide warning signage’s at the identified puroks with high susceptibility. Activate BDCC during periods of inclement weather. |
| 40. Buenavista | Moderate | Monitor and observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Evacuation of residents especially at areas near base of slope during periods of heavy rains. Establish a no-settlement buffer zone at areas where landslide had previously occurred (ex. Behind the Catholic Chapel and the INC chapel at Purok 6). Installation of landslide warning signage’s at the identified puroks with moderate susceptibility. Activate BDCC during periods of inclement weather condition. |
| 41. Cagutsan | High; Puroks 1,2,3 | Evacuation of residents especially at areas near rivers and streams due to potential of landslide from undercutting of base of slope by river erosion. Activate BDCC during periods of inclement weather condition. |
| 42. Cantiasay | Moderate, Purok 6 and 7 | Monitor and observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Install warning signages along the road sections of the purok identified as unstable for safetly of motorists and passers-by. Activate BDCC during periods of inclement weather condition. |
| 43. Catadman | Low | Monitor possible reactivation of an old tension crack noted in part of the barangay and restrict future development of settlements in the area. Activate Barangay Disaster Coordinating Council (BDCC) in other hazards that may occur (e.g. storm surge, tsunami) |
| 44. Danawan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). Restrict future settlements in area where a debris slide previously occurred. Activate Barangay Disaster Coordinating Council (BDCC) in other hazards that may occur (e.g. storm surge, tsunami) |
| 45. Libuac | Moderate; Puroks 1 3,4,6 | Monitor and observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Evacuation of residents especially at areas near base of slope during periods of heavy rains. Establish a no-settlement buffer zone at areas where landslide had previously occurrred. Installation of landslide warning signage’s at the identified puroks with moderate susceptibility. Activate BDCC during periods of inclement weather condition. |
| 46. Lisondra | Low | Activate Barangay Disaster Coordinating Council (BDCC) in other hazards may occur (e.g. coastal flooding, storm surge, tsunami) |
| 47. Manyagao | High; Purok 4 | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Evacuation of at least 14 houses at Purok 4 on the southeast portion of Manjagao near the base of a 40-50 meter high and steep slope during periods of heavy rains and long-term relocation. Installation of landslide warning signage’s at the identified puroks with high susceptibility. Activate BDCC during periods of inclement weather. |
| 48. Nonoc / Talisay | High; Purok 3, 5 and Mining Area 5 | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Installation of landslide warning signage’s at the identified puroks with high susceptibility. Activate BDCC during periods of inclement weather and initiate prompt evacuation scheme at identified vulnerable areas /puroks. |
| 49. San Jose | High; Purok 1, 3, 4 | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Installation of landslide warning signage’s at the identified puroks with high susceptibility. Activate BDCC during periods of inclement weather and initiate prompt evacuation scheme at identified vulnerable areas /puroks. |
| 50. San Pedro | Low | Activate Barangay Disaster Coordinating Council (BDCC) in other hazards may occur (e.g. coastal flooding, storm surge, tsunami) |
| 51. Sidlakan | Moderate; Purok 3 | Monitor progress of mass movement (e.g. landslides, tension cracks) esp. that observed in Purok 3 where three houses could be affected. Activate BDCC during periods of inclement weather and initiate evacuation scheme at identified vulnerable areas. |
| 52. Sugbay | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Activate BDCC during periods of inclement weather condition. |
| 53. Talisay | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Installation of landslide warning signage’s at the identified puroks with high susceptibility (ex. Mining 5 area). Activate BDCC during periods of inclement. |
| 54. Zaragosa | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Observed for saturated ground or seeps in areas that are not typically wet. Activate BDCC during periods of inclement weather condition. |

Table 13

Summary of the Assessment of the Municipality of TAGANAAN

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Laurel | High | Monitor progress of mass movements (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device / system; Identify evacuation site/ escape routes in case of extreme weather conditions; Activate BDCC during continuous heavy rains and alert people living along the slopes particularly in Puroks 4 & 5. |
| 2. Banban | High | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify other evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Brgy. Officials and residents should always be vigilant especially during the rainy season; Immediate and temporary evacuation during heavy rainfall; Activate BDCC in your area. |
| 3. Union | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Constant communication and updates with Brgy. Laurel on geohazard situation; Alert residents on Purok 1 on possible landslide occurrence ; Activate BDCC in your area. |
| 4. Aurora | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Develop an early warning device/system; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Activate BDCC in your area |
| 5. Upper Libas | Low | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 6. Lower Libas | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 7. Sampaguita | None | Appropriate river embankment structure has to be constructed along the major river draining the brgy. area to avert further scouring and erosion of the riverbanks. |
| 8. Himamaug | None | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 9. Azucena | None | Warn residents of Puroks 1,2,5 and 6 on flooding hazards. Evacuate residents from low-lying (flood-prone areas) during extreme weather conditions. |

### Table 14

### Summary of the Assessment of the Municipality of TUBOD

| Barangay | Landslide Susceptability Rating | Recommendations |
| --- | --- | --- |
| 1. Del Rosario | Moderate | Monitor progress of mass movements (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks) particularly in Purok 7; Develop an early warning device / system; Identify evacuation site/ escape routes in case of extreme weather conditions; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); Observe for saturated ground or seeps in areas that are not typically wet; Activate BDCC during continuous heavy rains and alert people living along the slopes. |
| 2. San Isidro | Moderate (Puroks 3 and 4) | Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) Observe for saturated ground or seeps in areas that are not typically wet; Activate BDCC during incremental weather condition. |
| 3. San Pablo | Moderate (Sitio Bongbong, Purok Santan) | Monitor progress of mass movement (e.g. landslides, tension cracks); Observe for presence of mass movement (e.g. landslides, tension cracks); Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet; Activate BDCC in your area. |
| 4. Capayahan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks); Observe for saturated ground or seeps in areas that are not typically wet; Activate BDCC during incremental weather conditions. |
| 5. Cawilan | Low | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content); |
| 5. Timamana | None |  |
| 6. Motorpool | None |  |
| 7. Marga | None | Warn residents of low-lying areas in Puroks 2, 3 and 4 (flood-prone) to evacuate to safer grounds during extreme weather conditions. |
| 8. Poblacion | None | Warn residents of low-lying areas (flood-prone) to evacuate to safer grounds during extreme weather conditions. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment period. Hence, the landslide susceptibility rating could advance (e.g. low to moderate, moderate to high) as the mass movement e.g. tension cracks progresses. Thus, the MGB constantly recommends strict and continuous monitoring by the barangays.

Prepared By:

### ROMEO M. DALODADO

Chief Geologist

MGB Rapid Geohazard Assessment Team Leader

July 17, 2006